## Slide 1: CS350 Project Progress Report Project Topic: Write a device driver for a simple device
Group Members: Hasan Erdem Bilgin, Yamaç Demirkan Yılmaz, Peker Çelik

## Slide 2: Background Research
USB Devices are usually more complex than one would think. Thankfully, the Linux kernel has a USB Core subsystem that handles the majority of the complexities. It provides us functions such as probe, disconnect, etc.

## Slide 3
USB Devices typically consist of configurations which are made of interfaces. Each interface has at least one endpoint.

## Slide 4
There are four types of endpoints:
Control: for configuring, retrieving information, sending commands and retrieving status reports
Interrupt: for transferring small amounts of data at a fixed rate, preferable for transferring time-sensitive data
Bulk: for transferring large amounts of bulk data
Asynchronous: also for transferring large amounts of data but the data is not always guaranteed to make it through, preferable for devices where constant data-flow matters, such as audio devices
- Every endpoint type is unidirectional except for control. Control is bidirectional.
- All USB devices always have the default control endpoint point 0.

## Slide 5: Our USB Device (split into columns)
Bus 001 Device 009: ID 05dc:a81d Lexar Media, Inc. LJDTT16G [JumpDrive 16GB]
Couldn't open device, some information will be missing
Device Descriptor:
bLength 18
bDescriptorType 1
bcdUSB 2.00
bDeviceClass 0
bDeviceSubClass 0
bDeviceProtocol 0
bMaxPacketSize0 64
idVendor 0x05dc Lexar Media, Inc.
idProduct 0xa81d LJDTT16G [JumpDrive 16GB]
bcdDevice 11.00
iManufacturer 1
iProduct 2
iSerial 3
bNumConfigurations 1
Configuration Descriptor:
bLength 9
bDescriptorType 2
wTotalLength 0x0020
bNumInterfaces 1
bConfigurationValue 1
iConfiguration 0
bmAttributes 0x80
(Bus Powered)
MaxPower 200mA
Interface Descriptor:
bLength 9
bDescriptorType 4
bInterfaceNumber 0
bAlternateSetting 0
bNumEndpoints 2
bInterfaceClass 8 Mass Storage
bInterfaceSubClass 6 SCSI
bInterfaceProtocol 80 Bulk-Only
iInterface 0
Endpoint Descriptor:
bLength 7
bDescriptorType 5
bEndpointAddress 0x81 EP 1 IN
bmAttributes 2
Transfer Type Bulk
Synch Type None
Usage Type Data
wMaxPacketSize 0x0200 1x 512 bytes
bInterval 255
Endpoint Descriptor:
bLength 7
bDescriptorType 5
bEndpointAddress 0x02 EP 2 OUT
bmAttributes 2
Transfer Type Bulk
Synch Type None
Usage Type Data
wMaxPacketSize 0x0200 1x 512 bytes
bInterval 255

## Slide 6: Observations
We observe that our USB Device’s model is Lexar Media, Inc. LJDTT16G [JumpDrive 16GB] and its vendor id and product id are 05dc and a81d respectively.
It has one configuration which consists of one interface which contains two endpoints of type bulk.
These two endpoints can handle a total of 1 kilobyte of data at once.

## Slide 7: Structure of Our Driver Module (my_usb.c)
//buraya struct usb_driver ve device table

## Slide 8: “__init” and “__exit” methods
Static method init stands for initialize and contains the functionality that we want to execute when the device is connected such as registering our device etc. . Takes no parameter.
Static method exit is used for the computation that we want our kernel to do when the device is disconnected. In our case we may disable some features of system or enable them.

## Slide 9
static int my_usb_probe(struct usb_interface *interface, const struct usb_device_id *id)
{
return 0;
}
  Probe function takes a usb interface and a usb device id as arguments and returns a int. This function gets called whenever any device supported by this driver gets installed to the host device.
static void my_usb_disconnect(struct usb_interface *interface)
{
}
  Disconnect function takes only a usb interface as an argument and doesn’t return anything. This function gets called whenever any device supported by this driver gets removed from the host device.
Probe and disconnect functions will be filled later.

## Slide 10: System Specifications
Operating System: Ubuntu 20 LTS
CPU Model: Intel Core i7 9th Generation
Device model: Monster Tulpar T7 V20.1

## Slide 11: Software Setup
No additional setup is required

## Slide 12: References
https://www.oreilly.com/library/view/linux-device-drivers/0596005903/ch13.html
https://kernel.readthedocs.io/en/sphinx-samples/writing_usb_driver.html
http://matthias.vallentin.net/blog/2007/04/writing-a-linux-kernel-driver-for-an-unknown-usb-device/
https://sysplay.github.io/books/LinuxDrivers/book/Content/Part11.html